X-ray spectroscopy. Emission spectra of metals

---
Registration of x-ray spectra
Energy-dispersive X-ray spectroscopy
Wavelength-dispersive X-ray spectroscopy
Semiconductor detectors:
Si(Li)
Silicon Drift Detectors
PiN diodes
+
Multichannel analyzers
Bragg diffraction at single crystal monochromator
+
Scintillation counter
Geiger counter

---
Miller indeces

---
For NaCl-type crystals oriented
Along main axis: (002), (004)...
Extinction rules for cubic lattices:
Primitive: all present
Body-centered: h+k+l=even
Face-centered: all odd or all even

---
Geiger-Muller tube